## Slide 1: Why a bitmap (.bmp), not a .jpg? If you cannot save a .bmp, make it an uncompressed .tif. This image is of mouse egg labeled with metal nanoparticles – it is a light micrograph with the display table inverted (dimmer light appears white with inverted display).
Compression (of this 8-bit 397,000 pixel image):
none (397kb memory) medium (12kb) high (5kb)
.bmp
.jpg
.jpg
Caution: powerpoint software has resampled these images, blurring image pixels so that original resolution is lost, see next slide for clear example

## Slide 2
Transmitted light micrograph (non-inverted display table)
Scanning electron micrograph
true pixels (visible with screen capture)
.pptx blurred
true pixels (visible with screen capture)
.pptx blurred

## Slide 3: The digital bitmap
We have a map of pixels, each with a coordinate in and y (and sometimes z). Each also has an intensity value defined by the bits of computer memory.
BITMAP A Cartesian or Gaussian map of intensities (bits). We can think of 3D data as stacks of 2D maps. (not always the case).
x
y
z

## Slide 4: First must identify and quantify object space and image space
-Dimensions of object space
-Dimensions of image space
-Dimensions of each data point (pixel or voxel) in image space
Using the above information, how do we define magnification?

## Slide 5: What is digital image data (bit depth)? Each pixel has a value, the more possible values a pixel has (bit depth), the more depth it is said to have.
0
0
180
0
0
180
180
180
180
255
255
255
255
120
120
120
How much memory will this (8 bit pixel depth) image consume?
Each pixel gets 8 bits of storage space. 8 bits = 1 byte of memory.
Base 2 math
2 levels, black or white 1 bit
256 levels of grey 8 bit
(or any other color)
65536 levels (check the # 16 bit of the last row of an .xls file)
16.7 million levels 24 bit or 3 x 8 bit (usually it is 8 bits each Red Green & Blue)
this is a representation of an 8-bit image, total of 16 pixels. This looks like a greyscale Look Up Table (LUT). See below.
When given image data (a photo, drawing, or micrograph), the display computer must look at the chosen LUT to know how to display the data.

## Slide 6
8 bit image – each pixel is ranked 0-255
24 bit image - 3 - 8 bit images overlaid (~16.8 million colors)
Usually Red + Green + Blue
y n
20 y or n 1 0
21 y or n 2 0
22 y or n 4 0
23 y or n 8 0
24 y or n 16 0
25 y or n 32 0
26 y or n 64 0
27 y or n 128 0
In digital data we talk about each bit being a 1 or 0 (yes or no). See the table at left and notice how you can get to any number between 0-255 by combining the 8 bits (y or n) of data.
1 byte computer memory = 8 bits
  1 bit (21) = 2 tones
  2 bits (22) = 4 tones
  3 bits (23) = 8 tones
  4 bits (24) = 16 tones
  8 bits (28) = 256 tones
  16 bits (216) = 65,536 tones
  24 bits (224) = 16.7 million tones
the numbers below depict a single 8-bit byte, each pixel gets one of these bytes in an 8 bit image

## Slide 7
The levels of 0-255 in an 8 bit image must each be assigned a color or intensity, only 256 different colors or intensities are available. An RGB or ‘true color’ image combines levels of red, green, & blue to give almost 17,000,000 color variations (this coding includes intensity and color).
The only way to know what object information a digital image represents (8 or 24 bit) is to know what sort of detector system collected the signal from the sample.
http://www.voteview.com
http://www.wit.ie/Research/ResearchGroupsCentres/Groups/MPRG/AgeRelatedMaculaDegeneration/RadiationAndAMD/ElectroMagneticSpectrum.jpg

## Slide 8: 8 bit Look up table from image J
0-255 data levels on x axis
0-255 display levels on y axis
this display level bar shows 256 levels of grey, this is probably greys.lut in image J
255
0
255

## Slide 9
data column | display columns
one channel only | 
 | Red Green Blue
0 | 0 0 0
1 | 1 1 1
2 | 2 2 2
3 | 3 3 3
. | . . .
. | . . .
128 | 128 128 128
. | . . .
. | . . .
255 | 255 255 255
data column | display columns
one channel only | 
 | Red Green Blue
0 | 0 0 0
1 | 0 0 1
2 | 0 0 2
3 | 0 0 3
. | . . .
. | . . .
128 | 0 0 128
. | . . .
. | . . .
255 | 0 0 255
data column | display columns
one channel only | 
 | Red Green Blue
0 | 0 0 0
1 | 1 0 0
2 | 2 0 0
3 | 3 0 0
. | . . .
. | . . .
128 | 128 0 0
. | . . .
. | . . .
255 | 255 0 0
data column | display columns
one channel only | 
 | Red Green Blue
0 | 0 255 0
1 | 1 1 1
2 | 2 2 2
3 | 3 3 3
. | . . .
. | . . .
128 | 128 128 128
. | . . .
. | . . .
255 | 255 0 0
GREY LUT
BLUE LUT
RED LUT
SETCOL LUT
8-bit data is defined by the imaging device and data storage devices
8-bit display palate is defined and limited by the display computer hardware and software. For example, a grey scale monitor cannot display all the colors of the rainbow!
If we were to use a greyscale monitor, the LUT (display columns shown at left) would not require separate display columns for R, G, and B because only grey is possible, one display column would suffice
Try to make different LUTS with image J LUT editor
256 levels/pixel
256 levels/pixel
256 levels/pixel
256 levels/pixel
These squares do not represent individual pixels. Each box is one of the possible display tones that can be assigned to any pixel in the image.

## Slide 10
data column | display columns
one channel only | 
 | Red Green Blue
0 | 0 255 0
1 | 255 0 0
data column | display columns
one channel only | 
 | Red Green Blue
0 | 255 255 255
1 | 0 0 0
1-bit data
usual 1-bit display is black or white but it can be any 2 colors or shades that the display hardware can display
24-bit display is considered not to have a single LUT. In reality, it must have some type of display LUT for each of its 3 8-bit data channels, total 24-bit data. That is, the PC/display must have a LUT for each color, then combine them via display hardware
B&W LUT
R&G LUT
data column | display columns | data column | display columns | data column | display columns
channel 1 | Red Green Blue | channel 2 | Red Green Blue | channel 3 | Red Green Blue
0 | 0 0 0 | 0 | 0 0 0 | 0 | 0 0 0
1 | 1 0 1 | 1 | 0 1 0 | 1 | 0 0 1
2 | 2 0 0 | 2 | 0 2 0 | 2 | 0 0 2
3 | 3 0 0 | 3 | 0 3 0 | 3 | 0 0 3
. | . . . | . | . . . | . | . . .
. | . . . | . | . . . | . | . . .
128 | 128 0 0 | 128 | 0 128 0 | 128 | 0 0 128
. | . . . | . | . . . | . | . . .
. | . . . | . | . . . | . | . . .
255 | 255 0 0 | 255 | 0 255 0 | 255 | 0 0 255
This spreadsheet is set up as a typical, 3 channel, 24-bit, Red, Green, Blue color image.
2 levels/pixel
2 levels/pixel
16.8 million levels/pixel

## Slide 11
The M.U. MRC-1024 has 3 emission channels (3 PMT detectors) with spectral resolution of 30-40nm as defined by our filters
598/40nm
R
G
B
522/35nm
680/32nm

## Slide 12: Voxels are 3D or volumetric pixels