GLY 320L

Lab 5

Trace Element Analysis of water samples

You are given 3 samples of water collected from two streams (and a subsidiary) in OH suspected of having been affected by acid mine drainage. You are required to analyze all 3 samples for the element Cd after standardization using the ZGFAAS. You are also given other analytical data on these streams that may be relevant. You are then requested to write a one-page summary of your results and how they compare to the standards of drinking water/ stream water as established by EPA, and the results obtained for other contaminants (e.g. As and Pb), pH, and conductivity (see attached tables).

Samples provided:

These were all collected from Lawrence County from the Slope Hollow area. The sketch below shows the relation of these to an abandoned coal mine.

Source Stream

Stream 1

Stream 2

Results

Table 1

| Stream | Fe (ppm) | Al (ppm) | Mn (ppm) | Pb (ppb) | As (ppb) |
| --- | --- | --- | --- | --- | --- |
| Source Stream | 133.80.21 | 29.62±0.13 | 5.342±0.32 | 0.44± 0.06 | 52.91± 10 |
| Stream 2 | 8.625± 0.083 | 14.47±0.064 | 3.303±0.14 | 1.02± 0.18 | 14.2± 0.6 |
| Confluence | 0.7291±1.86 | b.d. | 1.357±0.49 | 0.49 ± 0.19 | 3.37± 0.5 |
| Stream 1 | 0.2661± 0.22 | 0.3562±1.8 | 1.014±0.19 | 0.87± 0.18 | 13.08 ± 4.4 |

b.d.: below detection

Table 2

| Stream | pH | Conductivity 19-Dec-07 (ppm) | Conductivity 29-Jan-08 (ppm) | Conductivity 6-Apr-08 (ppm) |
| --- | --- | --- | --- | --- |
| Source Stream | 3.99 | 1060 | 930 | 950 |
| Stream 2 | 3.99 | 640 | 600 | 510 |
| Confluence | 6.11 | 330 | 380 | 250 |
| Stream 1 | 6.6 | 280 | 350 | 180 |

# Text boxes

Portal to abandoned mine

Source stream

Stream 1

SR-93

Stream 2

N